## Slide 1: Distributed Processing Technology Technical Presentation
John Kearney, Technical Support Manager
407-830-5522
email: kearney@dpt.com
Notes: 1
1
1

## Slide 2
"DPT is a leading supplier of high
array solutions and storage management
software for the microcomputer industry."
performance peripheral controllers, disk
Notes: 2
2
2

## Slide 3: How To Contact DPT Technical Support
6AM - 6PM Monday-Friday (GMT -05:00)
407-830-5522 tel. - 407-260-5366 fax
Internet - “support@dpt.com”
Web - www.dpt.com
Anonymous ftp - ftp.dpt.com
Notes: 6
10
10

## Slide 4: General SCSI Guidelines
A - Maximum Cable Length:
- 3 Meters (10 feet) @ 10Mhz
B - Stub Spacing:
- Minimum 12 inches between connectors
Unique SCSI ID for each device
Each end of the Bus requires termination
Each terminated device to supply term power
A
B
Page 55
Notes: 7
24
27

## Slide 5: Types of Termination
Passive Termination 220-ohm Pull Up Resistor from TERMPWR & Signal Line 330-ohm Pull Down Resistor from GND & Signal Line 132-ohm Resultant Impedance
Active Termination Voltage Regulator (2.85v) 110-ohm Resistor on each Signal Line
Forced Perfect Termination (FPT) Compensates for Impedance Variations via Diode Switching and Biasing
Definition: Impedance Matching Circuit Designed to
Prevent Signal Reflections

## Slide 6: General SCSI Guidelines
CABLES LEFT UNTERMINATED ACT AS ANTENNA!!!
Signals that Reach An Unterminated SCSI Bus Encounter an
Infinite Resistance Source (AIR) & reflect back the other way.
Termination
Acts as Antennae
Controller
Page 55
Notes: 8
24
27

## Slide 7: General SCSI Guidelines
WHEN ATTACHING BOTH INTERNAL AND EXTERNAL DEVICES, CONTROLLER IS IN THE “ MIDDLE” OF THE BUS AND SHOULD NOT BE TERMINATED !
Termination
Controller
Page 55
Notes: 9
24
27

## Slide 8: Mixing Wide & Narrow SCSI
THINK OF WIDE SCSI AS TWO SEPARATE 8-BIT DATA PATHS EACH REQUIRING TERMINATION
Termination
Controller
HIGH 8-BIT
LOW 8-BIT
Page 55
Notes: 10
24
27

## Slide 9: Mixing Wide & Narrow SCSI
REMEMBER - BOTH LOW ORDER BITS AND HIGH ORDER BITS MUST BE TERMINATED !!
Un-Terminated HIGH 8-bits !!
Controller
HIGH 8-BIT
LOW 8-BIT
WIDE DEVICES
NARROW DEVICE
Page 56
Notes: 11
24
27

## Slide 10: Mixing Wide & Narrow SCSI
EXTERNAL DEVICE TERMINATES LOW & HIGH BITS
INTERNAL DEVICE TERMINATES LOWER 8 BITS
CONTROLLER SET FOR “HIGH ONLY” TO TERMINATE HIGH 8 BITS
Termination
Controller
HIGH 8-BIT
LOW 8-BIT
WIDE DEVICES
NARROW DEVICE
Page 56
Notes: 12
24
27

## Slide 11: Narrow vs Wide SCSI
Data Width - 8 bit
Transfer Rate - 10 MHz
Max. of 7 devices
Uses a 50-pin SCSI Cable
Max. 3 Meters Total Cable Length @ 10 MHz
Minimum 12” Between Devices
Normal Rules of Termination Apply
Data Width - 16 bit
Transfer Rate - 10 MHz
Max. of 15 Devices
Uses a 68-pin SCSI Cable
Max. 3 Meters Total Cable Length @ 10 MHZ
Minimum 12” Between Devices
Normal Rules of Termination Apply
Page 56
Notes: 13

## Slide 12: Fast SCSI 2 vs Ultra SCSI
Data Width - 8 bit
Transfer Rate - 10 MHz
Max. of 7 devices
Uses a 50-pin SCSI Cable
Max. 3 Meters Total Cable Length @ 10 MHz
Minimum 12” Between Devices
Normal Rules of Termination Apply
Data Width - 16 bit
Transfer Rate - 20 MHz
Uses a 68-pin SCSI Cable
Max. 4 Devices evenly spaced w/3 Meter Cable Max 8 Devices evenly spaced w/1.5 Meter Cable
Normal Rules of Termination Apply
Page 56
Notes: 14

## Slide 13: SCSI Interface Comparison

## Slide 14
Hardware and Software Caching Overview
IV

## Slide 15: Cache Management Algorithms
Read Cache
Idle Writes
50 % Dirty
Monitor HOST’s IRQ Pending Line
Write Back Cache
Speculative Read-Ahead
Notes: 60
53
40

## Slide 16
OS Cache
Strategy
Application
program
OS
cache
Disk
Subsystem
Eliminate Disk Reads
Postpone Disk Writes
Notes: 61
54
41

## Slide 17
Application
program
OS
cache
Peripheral
controller
Reads : Writes
3 : 1
Reads : Writes
1 : 1
66% Read Hits
OS Cache Reduces Reads
All Writes Must be Written to Disk
Before CPU can Process Next Command
(900 : 300)
(300 : 300)
Notes: 62
56
43

## Slide 18
LIGHTLY LOADED
SERVER-CLASS SYSTEM
Bus activity:
Bus
Idle time
Application programs
write to OS cache:
OS cache flushes to disk:
(up to 20ms per write)
Bus
Idle time

## Slide 19
Larger OS Caches Produce
More Writes than Reads
Application
program
Software
cache
Peripheral
controller
READS : WRITES
3 : 1
READS : WRITES
1 : 3
90% read hits
(900 : 300)
(81 : 300)
Notes: 63
57
44

## Slide 20
SERVER-CLASS SYSTEM
WITHOUT HARDWARE CACHE
Bus activity:
Idle
time
Application programs
write to OS cache:
Idle
time
OS cache flushes to disk:
(20ms per write)

## Slide 21
SERVER-CLASS SYSTEM
WITH HARDWARE CACHE
System bus activity:
DPT’s IOP bus:
Idle
time
Application programs
write to OS cache:
OS cache flushes to DPT’s Cache:
(1ms per write)
Elevator-sorted writes go to disk:
(1-10ms per write)
Idle
time

## Slide 22
DPT’s
Intelligent I/O Processing
Combines I/O Requests
Sorts I/O Requests
Elevator Sorts Cached Writes
Notes: 64
60
47

## Slide 23
Disk Writes
Without
Elevator
Sorting:
15-20ms average
disk write
31
27
93
17
4
65
11
27ms
20ms
17ms
11ms
25ms
19ms
Notes: 65
61
48

## Slide 24
Disk Writes
With DPT’s
Elevator
Sorting:
1-6ms average
disk write
3
4
5
6
16
26
46
0.3ms
0.3ms
0.3ms
3ms
3ms
6ms
Notes: 66
62
49

## Slide 25
Result:
OS Cache:
Best For Improved Read Performance
DPT Cache:
Best For Improved Write Performance
Notes: 67
63
50

## Slide 26
Hardware vs. Software RAID
Software RAID...
Steals CPU cycles
OS dependent
May not be bootable
Causes additional I/O
Notes: 87
76
65

## Slide 27
SCSI Host Bus Adapters
Notes: 28

## Slide 28
Upgradable adapters with ‘Grow-as-you-Go’ architecture
for increased scalability and ease of use
Upgradable SCSI Adapters
PCI, EISA, ISA Adapters
Notes: 29

## Slide 29: DPT Product Number Structure
PM - Processing Module, Controller Card
RC - RAID/Caching Module, Adds RAID & Cache
SM - SIMM Memory Module, ECC Cache RAM
a b c d / e f
a - Controller’s Cache Status
b - Controller’s CPU
c - Controller Architechure
d - Host Bus Interface
e - Device Interface
f - Controller Floppy Option

## Slide 30
PCI
PM2044U
PM2044W
PM2044UW
PM2144W
PM2144UW
Page 11
EISA
PM2042W
PM2142W
ISA
PM2041W
All SmartCache IV are Cache/RAID Upgradeable
Processor is Either 68000 or 68020
Last Number in Part Number Indicates Bus Interface
4 = PCI, 2 = EISA, 1 = ISA
Notes: 33
36

## Slide 31
Firmware: One EPROM - 2 MB
SCSI BIOS ROM: Embedded in firmware
Supports up to 40 MB/s SCSI Bus Transfers
SCSI connectors:
- Internal 50-pin Berg header & 68-pin
high density connector
Controls up to 15 SCSI devices per HBA
Hardware cache and RAID upgradable
- External 68-pin high density connector
Motorola 68000/20 MHz Processor
132 MB/s PCI Bus Mastering Transfers
Upgradable Half slot design
FAST/WIDE
SCSI-3
PM2044U/W/UW
Page 11
Notes: 33
36

## Slide 32
Firmware: One EPROM - 2 MB
SCSI BIOS ROM: Embedded in firmware
High performance upgradable half slot design
Supports up to 40 MB/s SCSI BusTransfers
SCSI connectors:
- Internal 50-pin Berg header & 68-pin
high density connector
Controls up to 15 SCSI devices per HBA
Hardware cache and RAID upgradable
- External 68-pin high density connector
Motorola 68020/20 MHz Processor
132 MB/s PCI Bus Mastering Transfers
FAST/WIDE
SCSI-3
PM2144/W/UW
Page 11
Notes: 34
37

## Slide 33
Firmware: One EPROM - 2 MB
SCSI BIOS ROM: 256K
Upgradable half slot design
Supports up to 20 MB/s SCSI Bus Tansfers
SCSI connectors:
- Internal 50-pin Berg header & 68-pin
high density connector
Controls up to 15 SCSI devices per HBA
Hardware cache and RAID upgradable
- External 68-pin high density connector
Motorola 68000/20 MHz Processor
33 MB/s EISA Bus Mastering Transfers
FAST/WIDE
SCSI-3
PM2042/W
Page 11
Notes: 31
34

## Slide 34
Firmware: One EPROM - 2 MB
SCSI BIOS ROM: 256K
Upgradable half slot design
Supports up to 20 MB/s SCSI Bus Transfers
SCSI connectors:
- Internal 50-pin Berg header & 68-pin
high density connector
Controls up to 15 SCSI devices per HBA
Hardware cache and RAID upgradable
- External 68-pin high density connector
Motorola 68020/20 MHz Processor
33 MB/s EISA Bus Mastering Transfers
FAST/WIDE
SCSI-3
PM2142/W
Page 11
Notes: 32
35

## Slide 35
Firmware: One EPROM - 2 MB
SCSI BIOS ROM: 256K
Upgradable half slot design
Supports up to 20 MB/s SCSI Bus Transfers
SCSI connectors:
- Internal 50-pin Berg header & 68-pin
high density connector
Controls up to 15 SCSI devices per HBA
Hardware cache and RAID upgradable
- External 68-pin high density connector
Motorola 68000/20 MHz Processor
ISA 10 MB/s Bus Mastering Transfers
FAST/WIDE
SCSI-3
PM2041/W
Page 11
Notes: 30
33

## Slide 36
Option Modules
Notes: 35

## Slide 37
Single add-on Cache & RAID module attaches directly to the end of your SmartCache IV adapter
Four on-board SIMM sockets
Supports up to 64 MB hardware cache
Use DPT ECC SIMMs or Standard SIMMs (Standard 36-bit, or 32-bit 72-pin, single sided, low-profile SIMMs may be used.)
Built in support for RAID 0, 1 and 5
RC4040 RAID/Caching Module
Install first & largest SIMM in Slot # 1
Page 11
Notes: 36

## Slide 38
Single add-on Cache & RAID module attaches directly to the end of SmartCache IV adapter, in a half-slot design
Two on-board DIMM sockets, supports up to 32 MB hardware cache
Use DPT ECC DIMMs or Standard DIMMs (Standard 32-bit, 72-pin, single sided, low-profile.
Built in support for RAID 0, 1 and 5
RC4041 RAID/Caching Module
Install first & largest DIMM in Slot # 1
Page 11
Notes: 36

## Slide 39
DPT Error Correction Code SIMMs
SM4000/4
SM4000/16
When a SM4000 SIMM is installed, the advanced ECC
algorithm will protect the entire data path through the
adapter cache and other adapter hardware.
DPT ECC SIMMs are
available in a 4 MB or 16 MB
capacity
Page 12
Notes: 37

## Slide 40
SCSI RAID Controllers
SMARTRAID
IV
Notes: 28

## Slide 41
PCI
PM3334UW
IV
Page 15
EISA
PM3332UW
Cache & Hardware RAID Ready
68040 Processor
Multi-Channel Upgradeable
Monitors Temperature & Voltage of Host
Notes: 44

## Slide 42
Ultra Wide
Multi-
Channel
Motorola 68040/40 MHz Processor
132 MB/s PCI Bus Mastering Transfers
Firmware: Flash
SCSI BIOS ROM: Flash
Hardware cache & RAID ready
Supports up to 40 MB/s SCSI
Bus Transfers
Supports up to 15 SCSI devices
per channel
Monitors temperature and voltage of Server
Upgradable to support two or three channels
PM3334UW
IV
Page 15
Notes: 44

## Slide 43
Ultra Wide
Multi-
Channel
Motorola 68040/40 MHz Processor
33 MB/s EISA Bus Mastering Transfers
Firmware: Flash
SCSI BIOS ROM: One EPROM 256K
Supports up to 40 MB/s SCSI
Bus Tansfers
WIDE adapter model supports up
to 15 SCSI devices per HBA.
Monitors temperature and voltage of Server and SmartRAID
sub-system.
Upgradable to support two or three channels.
Hardware cache & RAID ready
PM3332UW
IV
Page 15
Notes: 43

## Slide 44
Upgrades SmartRAID controllers
to 2 or 3 Ultra Wide SCSI channels
Self-configuring, no switches or
jumpers
Used with PM3334 or PM3332
Channel Module
SX4030/1UW
SX4030/2UW
IV
Page 15
Notes: 45

## Slide 45
DPT Error Correction Code SIMMs
SM4000/4
SM4000/16
When a SM4000 SIMM is installed, the advanced ECC
algorithm will protect the entire data path through the
adapter cache and other adapter hardware.
DPT ECC SIMMs are
available in a 4 MB or 16 MB
capacity
Page 12
Notes: 46

## Slide 46: Adapter Troubleshooting Techniques
SCSI BIOS ROM
  Obtain Peripheral Inventory List
  Verify HBA’s Firmware & BIOS ROM Versions
  Verify HBA I/O Port & IRQ Values
  Verify a Peripheral’s SCSI ID
HBA’s 10 Segment LED Bank
  BLINKLED Patterns (Occur During HBA Initialization)
  Normal Operation Definitions
Removal of Attached Modules
  RC4040 or RC4041 (SmartCache IV)
  SX4030 (SmartRAID IV)

## Slide 47: SCSI BIOS ROM MESSAGE
DPT SCSI BIOS Vx.x
Distributed Processing Technology
© Copyright 1990-1997
A
Controller:xxxx -R W /UW v0xx 4.0MB PORT:xxxx IRQ:xx
<CTRL-D> for DPT Configuration Utility
A = SCSI BIOS ROM (SmartROM) Version F = Installed Cache Amount
B = Controller Model Number G = I/O Adddress
C = RAID Enabled H = IRQ Setting
D = Wide/Ultra Wide SCSI Capable
E = Controller Firmware Version
B
C
D
E
F
G
H
Page 57

## Slide 48: LED BLINKLED Patterns
1
2
3
4
5
6
7
8
9
10
1 2 4 8
LSB
1 2 4 8
MSB
81 - LUNTBL’s Overlap System Stack
82 - SIMM #1 Too Small For Buffers
83 - SIMM #1 Is Missing
84 - SIMM #1 Is Parity w/ECC in 2,3, or 4
85 - Load CP DMA Swapped Words of CP
86 - EPROM Checksum Failure
87 - Memory Size Mismatch w/Hardware ID Bits
88 - SCSI Bus Reset Stuck More Than 1 Second
Page 60
Notes: 51
51
29

## Slide 49: LED BLINKLED Patterns (CONT)
1
2
3
4
5
6
7
8
9
10
1 2 4 8
LSB
1 2 4 8
MSB
89 - PCI MATO (Master Timeout Abort)
8A - Fatal SRAM Subordinate Master Abort
8B - Fatal SRAM Dominate Master Abort
8C - V2 RCTBL Internal Error
8D - SmartROM Image Is Missing or Corrupt
8E - NVRAM Has Been Erased*
8F - Mixture Of Parity & ECC SIMMs Detected
Page 60
Notes: 52
52
30

## Slide 50: LED Display Quick Reference
1
2
3
4
5
6
7
8
9
10
1 - Busy
2 - Computer Bus Xfer to Adapter
3 - Computer Bus Xfer From Adapter
4 - Cache Hit
5 - Disk Read Ahead Active
6 - Disk Read
7 - Disk Write
8 - Adapter Reset
9 - Adapter IRQ Pending to Computer
10 - DRQ Asserted to Computer
Page 19
Notes: 51
51
29

## Slide 51
SCSI Storage Solutions
IV
Notes: 53

## Slide 52
Flexible 'RAID-Ready' Solutions
Storage Management Software
SmartRAID Controllers
SmartRAID Intelligent Cabinet
and Hot-Swappable Drives
IV
Notes: 41

## Slide 53
Cabinet Temperature Status
Cabinet Power Status
RAID Array Status
Automatic Drive Removal/Insertion Detection (Automatic RAID Rebuild)
Visual Cabinet Status Indicators
Active Termination
IV
Sub-System Features

## Slide 54: RAID Station 3
Complete RAID Kit
  Three Hot Swap Locking Drive Bays
  Tower Enclosure
  Ultra Narrow or Ultra Wide PCI HBA
  RAID/Caching Module
  4 MB of Cache (Expandable to 64 MB)
  1 Meter External SCSI Cable
  Supports RAID Level 0, 1, 5, 0/1 & 0/5
Ultra Narrow
&
Ultra Wide
Page 16

## Slide 55
Tower Storage Cabinet
Supports up to 9 SCSI Devices
Split Bus Architecture Supports Duplexing
Redundant Power/Fans units
SCSI Carrier Devices and Power/Fan units are Hot Swappable
Reports Environmental Status
IV
Page 17
Notes: 54
78
75

## Slide 56
Intelligent “Hot-Swap” Devices
SCSI ID’s Auto Configurable Per Slot
Auto Terminating
4GB & 9GB Hard Drives (W & UW)
2/4GB & 4/8GB DAT Drives
IV
Page 17
Notes: 55
79
68

## Slide 57
“Hot-Swap” Carrier Design
Ground
Control
Data
IV
Notes: 56
80
69

## Slide 58
SmartRAID
Split SCSI Bus
Allows Duplexing Within Single Cabinet
SmartRAID
RAID-0
RAID-0
Netware/
Windows NT Duplexed
IV
Notes: 57
81
76

## Slide 59
Scalability
Add more disks to balance CPU and I/O performance
SmartRAID
RAID-5
Hot Spare
RAID-5
RAID-5
Notes: 58
82
87

## Slide 60
SmartRAID ECC Protects
entire RAID Subsystem
System
Bus
ECC
SCSI bus
SmartRAID
SmartRAID
DPT
Exclusive!
Notes: 59
83
88

## Slide 61
RAID
Redundant Array of Independant Drives
RAID is the only technology that
allows you to increase capacity
and performance proportionately!
and also add Disk Fault Tolerance...
Notes: 68
64
53

## Slide 62: Storing RAID Information
Two Generally Accepted Methods Controller NVRAM Reserve Area of Disks
Pros: No Disk Space Multiple Copies of Used RAID Configuration
SCSI Bus Integrity Controller Can Be Doesn’t Prevent Replaced & RAID Info is “reading” RAID Info Still Intact
Arrays & Hot Spares Can Be Created At Anytime
Cons: Single Point of SCSI Bus Integrity Can Failure Affect “reading” RAID Info
Page 21

## Slide 63: Storing RAID Information
DPT Uses HD Space to Store RAID Information
Reserve Block: The last 256K bytes of each HD attached to a DPT adapter
Hard Drives Included in an Array
RAID Level (RAID-0, 1, 5)
Stripe Size Used in the Array
Hot Spare Assignments
Stripe Sequence/Order of Hard Drives in An Array
Current Array Status (Optimal, Degraded, Rebuilding)
Caching Parameters Assigned to Hard Drives
Page 21

## Slide 64
In non-striped system
I/Os wait for single actuator
Drive 1
Drive 2
Drive 3
Drive 4
Drive 5
Notes: 71
66
55

## Slide 65
In a striped array, I/Os are
evenly distributed across drives
Drive 1
Drive 2
Drive 3
Drive 4
Drive 5
As more disks are added,
throughput increases...
Notes: 72
67
56

## Slide 66
DATA STRIPING
Logical data stripes are interleaved
across physical drives
Drive 1
Drive 2
Drive 3
Drive 4
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
Notes: 69
65
54

## Slide 67
STRIPING WITH ROTATING PARITY
Logical data and parity stripes
are interleaved across physical drives
Drive 1
Drive 2
Drive 3
Drive 4
1
2
3
P
4
5
P
6
7
P
8
9
P
10
11
12
Notes: 70
65
54

## Slide 68
DPT SUPPORTED RAID LEVELS
RAID 1:
RAID 0:
Non-Redundant Striped Array
Mirrored Array
RAID 5:
Striped Array with Rotating Parity
Notes: 74
69
58

## Slide 69
RAID 0
NON-REDUNDANT STRIPED ARRAY
DATA
DATA
DATA
DATA
DATA
DATA
Highest Bandwidth & Best Data Storage Efficiency
Simultaneous Reads & Writes Can Occur
on Each Hard Drive
Page 22 & 57
Notes: 75
70
59

## Slide 70
RAID 0
Physical Disk 1
Physical Disk 2
Logical Disk
(What Operating System can “see”)
Software Level
Single Write I/O to HW
Hardware Level
Controller “splits” Data to Physical Disks
10110011
0011
1011
Page 57
Notes: 76
71
60

## Slide 71
Highest Bandwidth With Fault Tolerance
Read Error Recovery & Repair
Read Closest Cylinder
RAID 1
MIRRORED ARRAY
DATA
DATA
DATA
DATA
DATA
DATA
Page 23 & 57
Notes: 77
71
60

## Slide 72
RAID 1
Physical Disk 1
Physical Disk 2
Logical Disk
(What Operating System can “see”)
Software Level
Single Write I/O to HW
Hardware Level
Controller duplicates Data to Physical Disks
10110011
10110011
10110011
Page 58
Notes: 80
71
60

## Slide 73
DATA/
PARITY
DATA/
PARITY
DATA/
PARITY
DATA/
PARITY
DATA/
PARITY
DATA/
PARITY
Slower on Writes & Recovery From a Hard Drive
Failure, Best Storage Efficiency of Redundant Arrays
RAID 5
STRIPED ARRAY WITH ROTATING PARITY
Page 24 & 58
Notes: 82
73
62

## Slide 74
RAID 5
Physical Disk 1
Physical Disk 2
Logical Disk
(What Operating System can “see”)
Software Level
Single Write I/O to HW
Hardware Level
Controller :
1 - Reads “old” Data
2 - Writes “new” Data
3 - Performs XOR
4 - Writes Parity
10110011
0000
1011
0011
Physical Disk 3
1000
XOR Parity Generation and Results
XOR
Page 58
Notes: 83
71
60

## Slide 75
RAID 5
UPDATING PARITY DURING WRITES
DATA
XOR
PARITY
XOR
WRITE
READ
READ
WRITE
Result: Each Write Causes 4 Additional I/Os
Plus 2 Math Operations
Page 59
Notes: 84
74
63

## Slide 76
RAID 5 - Error Recover
Physical Disk 1
Physical Disk 2
Logical Disk
(What Operating System can “see”)
Software Level - Single Read Request
Hardware Level
Controller :
1 - Reads Data / Parity
2 - Performs XOR
3 - Supplies Result to OS
10110011
?????
Physical Disk 3
1000
XOR Parity and Remaining data to
Re-Construct “lost” data
XOR
0011
1000
Page 59
Notes: 85
71
60

## Slide 77
Dual Level RAID - 0/1
Logical Disk
(What Operating System can“see”)
Raid-Capable DPT Driver Level
- Splits Data Between Hardware LSUs
10110011
1011
0011
Hardware Level
- Controller Duplicates Data to Physical Disks
1011
1011
0011
0011
Operating System Performs Single Write I/O to DPT Driver
DPT Driver Performs 2 Write I/Os to Controller
Page 59
Notes: 78
71
60

## Slide 78
Dual Level RAID - 0/5
Logical Disk
(What Operating System can“see”)
Raid-Capable DPT Driver Level
- Splits Data Between Hardware LSUs
10110011
1011
0011
Hardware Level
- Controller Performs XOR Operation, creates Parity, and writes Data/Parity to Physical Disks
1111
0100
1111
0011
Operating System Performs Single Write I/O to DPT Driver
DPT Driver Performs 2 Write I/Os to Controller
1100
1011
Page 59
Notes: 79
71
60

## Slide 79: Server OnCall The Next Level In Server Fault Tolerance
RAID Protects Your Data From a Drive Failure
Server OnCall Keeps Your Data Accessible Even If Your Server Fails or Locks-up
One On Call Monitor Can Protect Up To Three Different Servers (NT 4.0, NW 4.11, or SCO 5.04)
Communicates Via The SCSI Bus
When Failure Occurs, Server OnCall Takes Control of Shared Hard Drives/RAID Array

## Slide 80: Server OnCall The Next Level In Server Fault Tolerance Implementation Considerations
Multiple CPU’s
NIC’s
Mouse
Video
CPU Power of OnCall System
Method of Re-introducing Original Server After Failover

## Slide 81
Storage Manager
Kits Include:
SCSI Host Adapter
Storage Manager Software
Internal SCSI Cable
All DPT Device Drivers
Complete Documentation
IV
Notes: 88
84
32

## Slide 82
Add performance and uniqueness through software
Storage Manager Software
Notes: 89
85
89

## Slide 83
Storage Manager provides
all necessary subsystem functions
INSTALLATION
AUTOMATIC
SETUP
RAID
DIAGNOSTICS
PERFORMANCE
TUNING
LOGGING
ERROR
BROADCASTING
EVENT
SCSI Bus
SCSI Bus
SCSI Bus
Physical Configuration
Notes: 90
86
90

## Slide 84
Technical Training
Question & Answer Time
IV
Notes: 91
87
92